| METTLER TOLEDO | DATA BRIEF |
| --- | --- |
|  |  |  | IND560 Custom |
|  |  |  | Single Material Filling Controller |

| Specifications |
| --- |
| Dimensions |  | Height | Width | Depth | Shipping Weight |
|  | Enclosure | 406.4mm (16.0 in) | 406.4mm (16.0 in) | 152.4mm (6.0 in) | 14 kg (30 lb) |
| Enclosure | CRS ANSI 61 Gray, optional 304 stainless steel, certified TYPE 4/12 (ref. IP65) (pending) Mounts to wall using integrated brackets |
| Power | Universal power supply, 87 to 264 VAC at 49 to 61 Hz, 750 mA consumption maximum (560 terminal only) |
| Display | Vacuum fluorescent, 21mm weight display, graphical 128 x 64 dots |
| Keypad | 5 user-selectable softkeys; Clear, Tare, Print, Zero, navigation keyset; numeric keys |
| Scale Types | Analog Scale: 10 VDC excitation powers up to 8 350( load cells, 2 or 3 mV/V IDNet Scale: interface current high-precision K bases and platforms; optional power supply for older models |
| Performance | Maximum update rates: Analog to digital 366 Hz; target comparison (setpoint) 50 Hz; PLC interface 20 Hz |
| Connectivity | Standard: COM1 – RS-232/422/485 Optional: COM2 – RS-232 / RS-422 / RS-485, 10Base-T Ethernet TC/IP port |
| Serial Interface Protocols | Inputs: ASCII commands for Clear, Tare, Print, Zero; barcode; SICS level 0 Outputs: METTLER TOLEDO Continuous or Demand; continuous template using 1 of 5 configurable templates; report printing; interfaces external ARM100 Input/Output module, SICS level 0 |
| Options | PLC (one option): Allen-Bradley® Remote I/O, DeviceNet™, Profibus® L2 DP; Analog Output: 4-20 mA and 0-10 VDC |
| Operating Environment | -10°C to +40°C (14°F to 104°F), 10% to 95% relative humidity, non-condensing |
| Agency Approvals (IND560 Terminal) | Weights and Measures | USA: Class II 100,000d; Class III/IIIL 10,000d; CoC 05-057 |
|  |  | Canada: Class II 100,000d; Class III/III HD 10,000d |
|  |  | Europe: Class II base dependent; III 7,500e, III 10,000e; includes alibi memory |
|  | Safety | cULus |
|  | Hazardous Area (pending) | Division 2 and 22: Class I and II, Groups A-D, F and G (pending) Zone 2 and 22: Class I and II, Groups IIC (pending) |

| Features | Benefits |
| --- | --- |
| Material Transfer Mode | Target comparison outputs for single or two-speed feeder control for both weigh-in and weigh-out applications Graphic display provides analog bar graph showing target status with and without weight value |
| Over / Under Mode | Graphic display indicates Under, OK and Over status with and without weight value Multiple methods of target and tolerance entry including barcode scanner, front keypad |
| Enclosure | Standard IP65 painted mild steel enclosure Optional 304 stainless steel enclosure provides required protection for harsh environments Heavy duty dual latches provide tamper resistant, reliable door seal |
| Status Lights and Push Buttons | Configurable, rugged push button options including Start, Tare, Jog, Print to meet unique application requirements Bright, LED lights provide visual queues to operators to minimize confusion and increase productivity |
| Ease of Navigation | Configure setup with menu driven, "Windows-like" navigation |
| Security | Supports the use of username with a password for setup security of four levels |
| Memory Tables | Target table stores up to 25 targets, each with tolerances and spill (preact) values Tare table stores up to 25 fixed tare values, each with accumulation |
| Programmable Softkeys | 15 programmable softkeys provide one-keypress access to target and tare tables, as well as functions such as start and pause to eliminate operator confusion and errors |
| PLC Connectivity | Optional PLC interfaces for A-B RIO, DeviceNet™, Profibus™ L2 DP or Analog Output installed inside the enclosure |
| Multiple Serial Protocols | Easy connection to remote display, PLC, DCS, and METTLER TOLEDO accessory modules |
| TraxDSP™ Filtering | Tunable digital filtering suppresses environmental effects on weighing accuracy |
| Global Approvals for Terminal | Provides acceptance in local markets |

| IND560 Custom Single Material Model Configuration |
| --- |
| Term. Type | Scale Type | # of operators | Wiring and Tags | Serial | PLC Interface | Software | Voltage for I/O | ARM100 | Hazardous Area | Enclosure | Custom |
| C56 | 1, 4 | 0-9 | 1 | 0, A | 0, A, B, P, D | 0 | 0, 1, 2 | 0, 2 | 0, 2 | M, S | 00-99 |
| C56 | 1 | 0 | 1 | A | 0 | 0 | 0 | 0 | 0 | M | 00 |

| Order Number | Description |
| --- | --- |
| IND560 Custom |
|  | Buttons (E-stop and Start included in all configurations) | Status Lights |
| 00 | None | None |
| 01 | Jog | None |
| 02 | Print | None |
| 03 | Tare | None |
| 04 | Jog, Print | None |
| 05 | Tare, Print | None |
| 06 | Jog, Tare | None |
| 07 | Jog, Print, Tare | None |
| 08 | None | Tolerance OK |
| 09 | Jog | Tolerance OK |
| 10 | Print | Tolerance OK |
| 11 | Tare | Tolerance OK |
| 12 | Jog, Print | Tolerance OK |
| 13 | Tare, Print | Tolerance OK |
| 14 | Jog, Tare | Tolerance OK |
| 15 | Jog, Print, Tare | Tolerance OK |
| 16 | None | Feed, Fast Feed, Tolerance OK |
| 17 | Jog | Feed, Fast Feed, Tolerance OK |
| 18 | Print | Feed, Fast Feed, Tolerance OK |
| 19 | Tare | Feed, Fast Feed, Tolerance OK |
| 20 | Jog, Print | Feed, Fast Feed, Tolerance OK |
| 21 | Tare, Print | Feed, Fast Feed, Tolerance OK |
| 22 | Jog, Tare | Feed, Fast Feed, Tolerance OK |
| 23 | Jog, Print, Tare | Feed, Fast Feed, Tolerance OK |

| IND560 Custom Scale Type |
| --- |
| 1 | Analog |
| 4 | IDNet |

| IND560 Custom Options (for field installation) |
| --- |
| 71209095 | Ethernet and 2 Serial Port Kit |
| 71209096 | PROFIBUS® L2 DP Interface Kit, Panel Mount |
| 71209098 | ALLEN-BRADLEY™ RIO Interface Kit |
| 71209099 | Analog Output Kit (4-20ma or 0 – 10V) |
| 72193580 | DeviceNet™ Interface Kit |
| 64055811 | Fill-560 Application Software |
| 71209352 | ARM100 Remote I/O Relay Module |
| 72185046 | IDNet Power Supply Adaptor Kit (for PIK-Brick weigh cells) |

| IND560 Custom # of Operators |
| --- |
| 0-9 | Defines how many total operators are installed |

| IND560 Custom Wiring and Tags |
| --- |
| 1 | Factory wiring of operators and nameplate tags |

| IND560 Custom Ethernet / Serial Option |
| --- |
| 0 | None |
| A | Ethernet TCP/IP Port and Two Serial Ports |

| IND560 Custom PLC Interface Option |
| --- |
| 0 | No output option |
| A | Analog Output (4-20 mA or 0-10 V) |
| B | Allen-Bradley RIO |
| P | PROFIBUS L2 DP Interface |
| D | DeviceNet Interface |

| IND560 Custom Application Software Option |
| --- |
| F | Fill560 Software |

| IND560 Custom I/O Voltage |
| --- |
| 0 | 110VAC |
| 1 | 220VAC |
| 2 | 24VDC |

| IND560 Custom ARM100 |
| --- |
| 0 | No remote ARM100 installed |

| IND560 Custom Hazardous Area |
| --- |
| 0 | Safe Area |
| 2 | Class 1 Division 2 / Zone 22 (future) |

| IND560 Custom Enclosure Material |
| --- |
| M | Painted Mild Steel |
| S | 304 Stainless Steel |